## Slide 1: Parenchymal Chamber for Liver Assist Device
December 5, 2011
Arjun Bahl, Ben Jiang, Cameron Hinkel
Group 28

## Slide 2: Part I: Need, Design Concept and Requirements

## Slide 3: Liver Disease
Affects 25 million Americans
  19 million cases involve viral hepatitis or cirrhosis
Major organ shortage
  ~7000 liver transplants each year
  16,200 remain on waitlist
  2000 will die this year waiting for a transplant

## Slide 4: Concept
An external hepatic liver device connected at the inlet to the Hepatic Portal Vein and at the outlet to the Inferior Vena Cava, such that it functions in parallel to the liver.
Consisting of a large number of subunits that each mimic natural blood flow in the capillary system of a liver lobule
A biomimetic vascular network has already been created

## Slide 5: Concept
Each subunit would consist of (1) an inlet, (2) parenchymal chamber,(3) membrane, (4) vascular network, and (5) outlet.
The scope of this project is the design of the parenchymal chamber.
The subunits are connected by a flow-header system.

## Slide 8: Design Requirements
Must provide 1% liver function
  Assume function proportional to number of cells
  Would match current State-of-Art
  Can keep a patient alive for approximately 2 weeks while waiting for transplant
Membrane pore size < 3 microns
  To prevent hepatic cell permeation through membrane
  FDA implications
Low total volume
  State-of-the art Liver Assist Device is a large bedside system taking up most of the room space, developed by Vital Therapies ©
  Should theoretically be scalable to > 1% liver function

## Slide 9: Design Requirements
Chamber requirements
  Adequate waste washout
    Normal Blood albumin concentration is 34-54 g/L
    Interstitial concentration is 10%-20%
  Current Problem: Cell death due to Pressure Buildup – A failed device by another group grew cells on the bottom of the membrane. Growing the cells on the top is our solution, which we have not discussed in previous reports for IP concerns.
  To optimize volume and achieve 1% percent liver function, maximize viable surface area per subunit

## Slide 10: Part 2: Design Analytics

## Slide 11: Maximizing Capacity
Liver contains 210 billion hepatocytes
Surface area of a hepatocyte:
A flat parenchymal chamber would fit ~1 million cells/subunit
2100 units base case

## Slide 12: Maximizing Capacity –Geometries
Shape | % Increase | Effective Increase (45* cutoff)
Square | 100% | 0%
Half Circle | 57% | 29%
Sinusoid | <41% | <41%
Quarter Circle | 11% | 11%
Trapezoid | 28% | 28%
Triangle | 41% | 41%
Show a calculation

## Slide 13: Viable Cell Growth on Vertical Surface
1 Day after Seeding 5 Days after Seeding
100x Magnification:

## Slide 14: Feature Arrangement
Parallel
Radial
Concentric

## Slide 15: COMSOL Model Parameters
Membrane Permeability
  Darcy’s Law
Albumin Boundary Condition
  Secretion rate in volume/surface area
Glucose Boundary Condition
  Consumption rate in volume/surface area
Albumin and Glucose Diffusion Constants

## Slide 16: COMSOL Model Parameters – Membrane Permeability
      Darcy’s Law: u = KΔP
Membrane | Permeability
 | (m/s*Pa)
PTFE 1um | 1.76E-07
Polycarbonate 0.4 um | 2.98E-08
Polycarbonate 1um | 3.14E-07
Polycarbonate 3um | 1.06E-06

## Slide 17: COMSOL Model Parameters – Albumin Secretion
Albumin secretion, rats: 2.14 mg/100 g/ hour
Hepatocytes 20uM diameter
Hepatocyte 70-80% of cytoplasmic mass of liver
Albumin mass: 67kDa
Albumin secretion: 1.98*10^-12 mol/(m^2*s)

## Slide 19: COMSOL Model Parameters – Other
Albumin Diffusion
  2*10^-8 m^2/s
Glucose Consumption
  1.6 pmol/min*μg protein
  1.38 mol/cm^2
Glucose Diffusion
  8*10^-8 m^2/s

## Slide 20: Summary of Results
Albumin removal
Glucose consumption

## Slide 21: Ridge Height
Based on physiological albumin levels found in literature, we decided to use a ridge height of 200 μm.

## Slide 22: Part 3: Design Details

## Slide 23: Ridge Dimensions
65 uM – large enough for proper seeding without increasing volume
200 uM – determined by albumin buildup

## Slide 24: Results
New surface area: 570 uM
Base case surface area: 170 uM
> 3 fold increase in viable surface area
Requires 626 units assuming maximum efficiency

## Slide 25: Cone Outlet

## Slide 26: Other Dimensions
100uM
570uM
1.35mm

## Slide 27: Other Dimensions
~14mm x 15 mm
Requires 9 layers assuming maximum efficiency: < 2L
Layer thickness: 5 mm

## Slide 28: Part 4: Materials and Manufacturing

## Slide 29: Subunit Assembly
Assembly of a single unit of the liver assist device begins with a 10:1 mixture of PDMS polymer to curing agent. This liquid PDMS is poured into each of 3 molds
Parenchymal Chamber mold depth: 0.5 mm
Vascular Network and Flow Header require placement of silicon tubing before mold is pored.

## Slide 30: Subunit Assembly
Molds are allowed to de-gas for 24 hours before being placed into an 85oC incubator for 1-1.5 hours to cure the PDMS

## Slide 31: Subunit Assembly
A 1mm hole is punched at the center of the vascular network and the flow header. The hole is punched from the featured face of the PDMS mold and goes through the top side of the silicone tube. The punch should not pass through the bottom side of the silicone tube or the rest of the PDMS.

## Slide 32: Subunit Assembly
A thin collagen film (Rat Tail, Type I) is applied to the roof of the chamber according to a complex, unpublished method developed in David Hoganson’s laboratory.

## Slide 33: Subunit Assembly
An extremely thin layer of liquid PDMS (about 10 microns) is stamped onto the featured faces of the flow header, vascular network, and parenchymal chamber. A piece of PCTE filter is carefully placed on the wet network face and the chamber is placed over the membrane. The flow header is glued in place beneath the vascular network layer. This assembly is placed in an 85oC incubator for 2 hours. A 0.5kg steel weight is placed on top of the assembly to insure a tight bond.

## Slide 34: Subunit Assembly
The inlet and outlet tubes are immediately attached to a pressurized perfusive media system with a 6 mmHg pressure drop provided across the network.

## Slide 35: Cell Seeding
Cell seeding is achieved through an inlet and outlet channel cut into the parenchymal chamber from the sides. Because of the complex surface geometry, the chamber must be seeded twice, once at a 45o angle relative to level and a second time at -45o relative to level. This ensures that hepatocytes adhere to the vertical faces of the chamber, hastening their growth to confluency over the entire surface area of the chamber. A solution of DMEM (Dulbecco’s Modified Eagle Medium) containing hepatocytes is flowed into the chamber. The concentration of cells is such that the seeding density is 100,000 cells/cm2. After seeding the inlet and outlet cuts are plugged up.

## Slide 36: Prices/Lead Times
PDMS
  Dow Corning Sylgard® 184 Silicone Elastomer Kit (~$50 for 1.1 lb kit, 3-4 kits required)
Silicone Tubing
  SILASTIC® Laboratory Tubing #508-003 (1.19mmOD, 0.64mmID) ($25/box)
PCTE Membrane
  Sterlitech - 1 micron pore size, 20x25mm, 30 pack ($330)
Molds
  Contract micro milling with Draper Laboratory
  $2500 for vascular network and parenchymal chamber
  $1500 for inflow header, outflow header, and seeding header
Cells
  C3A clonal derivative of HepG2 hepatocyte line – 1 vial from ATCC (American Type Culture Collection) ($280)
Total Lead time: 2-3 weeks

## Slide 37: Multi-Unit Assembly
In general
  3x3 Array of 8 subunits each
  For >626 subunits, requires 9 layers
Involves
  Additional Flow-Header level to maintain pressure across different stacks
  Additional Seeding level to seed assembled stack
Beyond Scope

## Slide 38: Part 5: Conclusions

## Slide 39: IP
Novel idea of growing cells on roof of Parenchymal Chamber
Without it, cells release waste into the chamber itself and pressure buildup kills cells

## Slide 40: Conclusions
Were we successful?
  We do have a fairly sophisticated model that we believe is robust enough to merit a prototype. However, it could be made more accurate with a more in depth study of target molecules like Urea, Carbon Dioxide, and Oxygen.
Future Directions?
  Increase quantity and sophistication of target molecule selection,
  Create macroscopic model of flow header system to make sure pressure remains fairly consistent across subunits
What did we learn?
  COMSOL, SolidWorks, CAD, Microfluidics, Engineering Design
What would we do differently?
  Work on a cloud to run simulations faster
For references, see accompanying paper