## Slide 1: Parenchymal Chamber for Biomimetic Liver Vascular Network
Building a Liver Assist Device
Arjun Bahl, Cameron Hinkel, and Ben Jiang – Group 28
Mentor: David Hoganson, MD

## Slide 2: Overview
Need
  Treatment of liver disease
Design
  Biomimetic vascular network
  Parenchymal cell chamber
Analysis
  COMSOL model
Details
  Specific parenchymal chamber design features

## Slide 3: Need

## Slide 4: Liver Disease
Affects 25 million Americans
  19 million cases involve viral hepatitis or cirrhosis
Major organ shortage
  ~7000 liver transplants each year
  16,200 remain on waitlist
  2000 will die this year waiting for a transplant
Need Design Analysis Details

## Slide 5: Addressing the Organ Shortage
All tissue engineering approaches prior to 1998 were angiogenesis dependent
Obvious need for vascular scaffold
Langer R, Vacanti J. Tissue engineering. Science 1993;260:920-926
Need Design Analysis Details

## Slide 6: Design

## Slide 7: Design overview
Need Design Analysis Details

## Slide 8: Design Choices: Chamber
Chamber height
  Transport of nutrients, waste
Surface geometry
  Surface area optimization
Surface coating
  Hepatocyte affinity to PDMS, collagen
Need Design Analysis Details

## Slide 9: Circumferential Orientation
64 micron deep triangular features
Surface area increased by 41%
Need Design Analysis Details

## Slide 10: Radial Orientation
64 micron deep triangular features at outer edge
Features converge toward center
Surface area increase is less than 41%
Need Design Analysis Details

## Slide 11: Design Choices: Membrane
Material
  Polycarbonate, PTFE
Thickness
Pore size
Porosity
Need Design Analysis Details
Membrane | Permeability [m2/(Pa·s)]
0.4μm PC | 2.98E-08
1.0μm PC | 3.14E-07
3.0μm PC | 1.06E-06
1.0μm PTFE | 1.76E-07

## Slide 12: Section Views (Liver Network)
Need Design Analysis Details

## Slide 13: COMSOL Model
Need Design Analysis Details
Three domains
Convective fluid flow
Species transport: Diffusion and convection
  Glucose, Albumin

## Slide 14: Equations
Darcy’s Law
  v = K ΔP
Flux of dissolved species
  Q = Qc + Qd
  Qc = v·C
  Qd = M(K·C1-C2)
Cell activity
  Glucose uptake proportional to local concentration
  Constant albumin secretion
Need Design Analysis Details

## Slide 15: Analysis

## Slide 16: Computational Analysis
Need Design Analysis Details

## Slide 17: Computational Analysis
Need Design Analysis Details

## Slide 18: Computational Analysis
Need Design Analysis Details

## Slide 19: Results
Need Design Analysis Details
Steady state operation
Triangular features increase surface area without impeding convection or diffusion
Sufficient glucose transport and albumin clearance occurs at most geometries
Optimal chamber depth
  36 μm to 100 μm

## Slide 20: Design Summary
Membrane
  3µm Polycarbonate membrane
  Maximal permeability
Chamber
  45° concentric triangular features
  36µm to 100µm depth
Need Design Analysis Details

## Slide 21: Responsibilities
Arjun
  Mathematical concepts
  Analyzing computational model results
  Final Presentation
Cameron
  Primary communications with David Hoganson
  Steering design considerations
  CAD drawings
Ben
  Experimental design
  Simulation parameters
  COMSOL
Need Design Analysis Details

## Slide 22: Schedule
Oct 26 Complete Progress Report
Nov 3 Expand to 3D Model
Nov 9 Refine Chamber Geometry
Nov 16 Run Extensive Simulations
Nov 29 Complete Design with all Modifications
Dec 2 Acquire total cost
Dec 7 Deliver final report
Need Design Analysis Details